Cable-Shift

Adjustments

VW

- Set the depth of the shift.  First disconnect the ¼” quick disconnect socket from the shift rod coupler ball and push the shift rod coupler into first gear (center gate, forward position).  Push the shift handle forward into the first gear position as well, now with a minimum of 3/16” of cable end threaded into the quick disconnect adjust the 5/8” jam nuts on the main cable, so the quick disconnect socket fits easily over the shift rod coupler ball.  Pull the shift rod coupler back (into second gear) and repeat adjustment until the shift handle functions through the middle of its travel.

- Set the gate position.  There are 3 gates in a 4-speed VW transaxle (4 gates in some 5-speed Porsche transaxles).  A gate and depth of shift diagram for VW 4-speed transaxle is shown below:

Push the shift rod coupler into first gear and loosen the two 7/16” jam nuts on the gate cable.  Gently slap the shift handle up against the Cable-Shift lock out bar.  Screw the 7/16” gate cable jam nuts towards one another and finger tighten against either side of the shift rod coupler block.  The Cable-Shift shifter should be close enough to ‘run through the gears’.  Shifting will improve when the engine is running and the clutch is depressed.  Shifting further improves as the synchronizers are worn in.

3.	Fine adjustment of the gate cable.  Fine adjustment of the gate cable is usually necessary after initial test drive, to make a smoother down shift from third to second without ‘catching’ reverse.  A diagram is provided to show this adjustment:

Small adjustments (1/6 of a turn) made with both jam nuts makes a noticeable difference.  A smooth shift sequence is therefore attainable first through fourth gears and reverse.

4.  	When the Cable-Shift shifter has been adjusted to the drivers ‘driving style’ under driving conditions, tighten all jam nuts, re-tighten bracket fasteners and recheck shifting sequence.

# Text boxes

Gate

1	      3

R	       2	             4

Depth

Of

Shift

Deeper into reverse

Gate Cable

Coupler Block

7/16” Jam Nuts

Out of reverse

Move coupler block on threads of cable